Front Yard

YES	NO		Street numbers easily visible from the street

YES	NO		Bushes, shrubs, and trees pruned away from

sidewalks, driveways, doors, windows, and gates.

YES	NO		Ground cover should be small gauge granite rock that

makes noise as you walk on it.  (River rock is not recommended.)

YES	NO		Limited or direct access to yard

YES	NO		Gates

1)  Locks Operable   ( ) YES   ( ) NO

YES	NO		Lighting covers the entire front of the house and all

hiding places.

1)  Motion Sensor Lighting   ( ) YES   ( ) NO

2)  Flood Lighting   ( ) YES   ( ) NO

Side Yards

YES	NO		Lighting adequately covers each entrance

1)  Motion Sensor Lighting   ( ) YES   ( ) NO

2)  Flood Lighting   ( ) YES   ( ) NO

YES	NO		Bushes, shrubs, and trees are pruned etc…

YES	NO		Gates

1)  Locks Operable   ( ) YES   ( ) NO

Back Yard

YES	NO		Lighting adequately covers each entrance

1)  Motion Sensor Lighting   ( ) YES   ( ) NO

2)  Flood Lighting   ( ) YES   ( ) NO

YES	NO		Bushes, shrubs and trees are pruned / trimmed, etc…

YES	NO		Gates

1)  Locks Operable   ( ) YES   ( ) NO

Detached Buildings (Garages, storage sheds, barns, etc…)

YES	NO		Locks on all doors (where applicable)

1)  Operable   ( ) YES   ( ) NO

YES	NO		Locks on all windows (where applicable)

1)  Operable   ( ) YES   ( ) NO

(1)

YES	NO		Lighting at all entrances (where applicable)

1)  Motion Sensor Lighting   ( ) YES   ( ) NO

2)  Flood Lighting   ( ) YES   ( ) NO

Garage Door:

YES	NO		Keep garage door closed when not in use

YES	NO		Garage door operating properly

YES	NO		Garage has an internal lock    Side door to garage

YES	NO		Door construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES	NO		Dead bolt with minimum off a 1” throw

YES	NO		Security strike plates

YES	NO		Door jams secure

YES          NO		Molding tight and secure

YES          NO		Hinges (pins on inside or otherwise secured)

YES          NO		Window (not recommended)

Living Room

Front Door Entrance:

YES         NO		Door Construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES         NO		Dead bolt lock with minimum 1” throw

YES         NO		Security strike plate

YES         NO  		With a minimum of 4 screws-each 2 ½” long

YES         NO		Door frame secure

YES         NO		Molding tight and secure

YES         NO		Hinges (pins on inside or otherwise secure)

YES         NO		Wide angle viewer (should be 190 degrees or better)

(2)

Double doors: (all rooms, all types)

YES         NO		Stationary door secured with metal flush bolts having

a minimum embedment of 5/8” into the head and threshold of the door frame.  Double doors shall also have an astragal (strong metallic cover slip) closing the space between double doors.

YES          NO		Security screen door

YES         NO		Recommended for all exterior doors.

Windows:		( ) Slider   ( ) Double Hung   ( ) Crank   ( ) Louver

YES	NO		Original locks in good condition

YES	NO		Auxiliary locks in place

( ) Pin lock   ( ) Keyed lock (recommended)

YES	NO		Anti-lift devise

(Screws in track above slider to prevent lift out.)

Glazing materials:

YES	NO		Applies to windows throughout residence

( ) Normal window glass

( ) Tempered glass   ( ) Plastic

Kitchen / Utility Room

Sliding Glass Doors (if any):

YES	NO		Original locks in good condition

YES	NO		Anti-slide device

( ) Keyed dead bolt

( ) Charlie Bar   ( ) Wood dowel

YES	NO		Anti-lift device

(Screws in track above slider to prevent lift out.)

Hinged Door:

YES	NO		Door construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES	NO		Dead bolt lock with a minimum 1" throw

YES	NO		Security strike plate

YES	NO		Door frame secure

YES	NO		Hinges (pins on inside or otherwise secured)

YES	NO		Wide angle viewer should be 190 degrees or better.

(3)

Double Doors, all rooms all types:

YES	NO		See description listed above (Applies to all types of double doors.)

Windows:		( ) Slider   ( ) Double Hung   ( ) Crank   ( ) Louver

YES	NO		Original locks in good condition

YES	NO		Auxiliary locks in place

( )  Pin lock   ( )  Keyed lock (recommended)

YES	NO		Anti-lift devises (Screws in track above slider to prevent lift out.)

Master Bedroom

Sliding Glass Doors (if any):

YES	NO		Original locks in good condition

YES	NO		Anti-slide device

( )  Keyed dead bolt

( )  Charlie Bar   ( )  Wood dowel

YES	NO		Anti-lift device (Screws in track above slider to prevent lift out.)

Hinged Door:

YES	NO		Door construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES	NO		Dead bolt lock with a minimum 1" throw

YES	NO		Security strike plate

YES	NO		Door frame secure

YES	NO		Hinges (pins on inside or otherwise secured)

YES	NO		Wide angle door viewer (should be 190 degrees or better.)

Double Door:

YES	NO 		See description listed above (Applies to all types of double doors.)

Windows:   		( ) Slider   ( ) Double Hung   ( ) Crank   ( ) Louver

YES	NO		Original locks in good repair

YES	NO		Auxiliary locks in place

( ) Pin lock   ( ) Keyed lock (recommended)

YES	NO		Anti-lift devises (Screws in track above slider to prevent lift out.)

(4)

Master Bathroom

Sliding Glass Door (if any):

YES           NO		Original locks in good condition

YES           NO		Anti-slide device

( ) Keyed dead bolt

( ) Charlie Bar   ( ) Wood dowel

YES          NO		Anti-lift device (Screws in track above slider to prevent lift out.)

Hinged Door:

YES           NO		Door construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES           NO		Dead bolt lock with a minimum 1" throw

YES           NO		Security strike plate

YES           NO		Door frame secure

YES           NO		Hinges (pins on inside or otherwise secured)

YES           NO		Wide angle viewer (should be 190 degrees or better)

Windows:		( ) Slider   ( ) Double Hung   ( ) Crank   ( ) Louver

YES           NO		Original locks in good repair

YES           NO		Auxiliary locks in place:

( ) Pin lock   ( ) Keyed lock (recommended)

YES           NO		Anti-lift devises (Screws in track above slider to prevent lift out.)

Bedroom # 2

Sliding Glass Doors (if any):

YES	NO		Original locks in good condition

YES	NO		Anti-slide device

( )  Keyed dead bolt

( )  Charlie Bar   ( )  Wood dowel

YES	NO		Anti-lift device (Screws in track above slider to prevent lift out.)

(5)

Hinged Door:

YES	NO		Door construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES	NO		Dead bolt lock with a minimum 1" throw

YES	NO		Security strike plate

YES	NO		Door frame secure

YES	NO		Hinges (pins on inside or otherwise secured)

YES	NO		Wide angle door viewer (should be 190 degrees or better.)

Double Door:

YES	NO 		See description listed above (Applies to all types of double doors.)

Windows:   		( ) Slider   ( ) Double Hung   ( ) Crank   ( ) Louver

YES	NO		Original locks in good repair

YES	NO		Auxiliary locks in place

( ) Pin lock   ( ) Keyed lock (recommended)

YES	NO		Anti-lift devises (Screws in track above slider to prevent lift out.)

Bedroom # 3

Sliding Glass Doors (if any):

YES	NO		Original locks in good condition

YES	NO		Anti-slide device

( )  Keyed dead bolt

( )  Charlie Bar   ( )  Wood dowel

YES	NO		Anti-lift devices (Screws in track above slider to prevent lift out.)

Hinged Door:

YES	NO		Door construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES	NO		Dead bolt lock with a minimum 1" throw

YES	NO		Security strike plate

YES	NO		Door frame secure

YES	NO		Hinges (pins on inside or otherwise secured)

(6)

YES	NO		Wide angle door viewer

(Should be 190 degrees or better.)

Double Door:

YES	NO 		See description listed above (Applies to all types of double doors.)

Windows:   		( ) Slider   ( ) Double Hung   ( ) Crank   ( ) Louver

YES	NO		Original locks in good repair

YES	NO		Auxiliary locks in place

( ) Pin lock   ( ) Keyed lock (recommended)

YES	NO		Anti-lift devises (Screws in track above slider to prevent lift out.)

Main Bathroom

Sliding Glass Door (if any):

YES           NO		Original locks in good condition

YES           NO		Anti-slide device

( ) Keyed dead bolt

( ) Charlie Bar   ( ) Wood dowel

YES          NO		Anti-lift devices (Screws in track above slider to prevent lift out.)

Hinged Door:

YES           NO		Door construction

( ) Solid core (hardwood 1 ¾” thickness)

( ) Metal clad

YES           NO		Dead bolt lock with a minimum 1" throw

YES           NO		Security strike plate

YES           NO		Door frame secure

YES           NO		Hinges (pins on inside or otherwise secured)

YES           NO		Wide angle viewer  (should be 190 degrees or better 0

Windows:		( ) Slider   ( ) Double Hung   ( ) Crank   ( ) Louver

YES           NO		Original locks in good repair

YES           NO		Auxiliary locks in place:

( ) Pin lock   ( ) Keyed lock (recommended)

(Screws in track above slider to prevent lift out.)

(7)

YES           NO		Anti-lift devises

Other/Miscellaneous

YES           NO		Automatic timers for lights and radios

Burglary Alarm Systems (if any):

YES           NO		( ) Monitored (Recommended)   ( ) Not monitored

( ) Locally (Recommended)   ( ) Out of state

*Audible Alarms are preferable

YES           NO		Emergency numbers by each phone

YES           NO		Grillwork/roller shields on high risk doors and windows

Operation Identification:

YES          NO		( ) Valuables marked with Drivers License Number?

Inventory  ( ) completed   ( ) incomplete

YES          NO		Safe for valuables

( ) Secured   ( ) Unsecured

Key control:

YES       NO		Keep track of existing keys

(Have house re-keyed if they are lost or stolen.)

YES       NO		Joined or started a Neighborhood Watch?

Recommendations:

______________________________________________________________________________________

______________________________________________________________________________________

______________________________________________________________________________________

______________________________________________________________________________________

Security Awareness Assessment submitted by:

___________________________         __                      ________   ______

Print Name / Signature					                      Date

DISCLAIMER:

KAUAI POLICE DEPARTMENT PROVIDES NO GUARRANTEES, WHETHER EXPRESSED, WRITTEN, OR IMPLIED THAT THE SUGGESTIONS AND RECCOMENDATIONS PUT FORWARD, IN CONNECTION WITH THE SECURITY AWARENESS ASSESSMENT, WILL MAKE YOUR HOME OR BUSINESS “BURGLARY-PROOF” AND OR PREVENT ANY TYPE OF CRIME AGAINST PROPERTY OR PERSONS WITHIN YOUR HOME OR BUSINESS.

(8)